## Slide 1: NDB Install Script

## Slide 2: What is supported?
The script will perform installation process for NXAPI switch.
Script has to run from switch only.
Script will perform following tasks—
  TCAM carving.
  Creating banner message.
It is supported for N9K , N3K series switches.

## Slide 3: NDB Install Script
NDB Install script will execute installation process require for NXAPI switches.
Using this script NXAPI switches will be added with all necessary configuration required during installation process.
Once configuration has been added successfully user has to manually reload the switch for the configuration to take effect.
The Script will not “reload “the Switch , and it’s the User responsibility to do it manually. But the Script will Intimate the Same.

## Slide 4: Install Script will perform following tasks
Enter Mode: Only accepted input from user will be nxapi or nx. This inputs are not case sensitive.
Create banner message: User have to enter banner message in the switch which starts and ends with delimiter character.
TCAM carving : User have to provide TCAM size for ifacl , ipv6-ifacl , mac-ifacl based on platform.
Note:
Script will perform validation for the below:
Weather Banner message is correct
Weather TCAM region got exhausted
Weather TCAM region value is correct

## Slide 5: NDB Install Script usage
Clone the code from the below link.
git clone https://github.com/datacenter/nexus9000.git
Navigate to following path:
cd nexus9000/
cd nexusdatabroker/

## Slide 6: To run script from switch
Login to nexus device.
Run the script using following command:- python path/ndb_nxos_install.py
Refer screen shot below—

## Slide 7: Trouble Shooting
Debug logs for the script can be displayed in 2 ways.
1) After running python script using following command :
python ndb_nxos_install.py
Logs will be shown only in log file
2) After running python script using following command :
python ndb_nxos_install.py --debug
Logs will be shown in console and in log file.
3) Log file name – ndb_nxos_install.log
4) Location – Log file will be created in bootflash directory. (/bootflash)
Cont…

## Slide 8: Trouble Shooting
Log file name , location--
Log file name – ndb_nxos_install.log
Location – Log file will be created in bootflash directory. (/bootflash)
How to open file --
To open log file in switch execute following steps-
1. Enter bash mode – run bash.
If in case bash mode feature is not enable then follow commands—
a. conf t
b. feature bash-shell
2. After entering the bash mode open log file using—
vi /bootflash/ndb_nxos_install.log
Cont….

## Slide 9: Trouble Shooting
Refer screen shot below to enable bash feature in switch
Refer screen shot below to open log file in switch—

## Slide 10: Recommendations
If we do telnet connection to the switch , sometimes python API’s gets hanged and you won’t see any output in console. It is recommended to run the script using ssh connection to the device.