## Slide 1: TLS NXAPI and Openflow scripts

## Slide 2: What is supported?
Switch mode |  |  |  | 
NXAPI | Single NDB and Single switch | Single NDB and multiple switches | Multiple NDB and single switch | Multiple NDB and multiple switches
Openflow | Single NDB and Single switch | Single NDB and multiple switches | Multiple NDB and single switch | Multiple NDB and multiple switches

## Slide 3: What is supported?
All controllers should have the same HA clustering configuration information in the config.ini files
In HA mode the information which is provided in first block of input file will be treated as Master .Remaining servers will be treated as a Slaves.
The tool will work for both default(admin) and non-default(other password) password of NDB.
The tool will not work for non-default username (By changing the username admin to something else ).
If user wants to run application for non-default password. User has to do following things-
a) Run NDB.
b) Change NDB password(No need to save configuration if auto-save feature is present).
c) Stop NDB Application.
d) Provide NDB login credentials in input file.
d) Run the python script.
Restriction for NXAPI
We can connect maximum 10 devices at a time.

## Slide 4: TLS NXAPI and Openflow
TLS Configuration Tool will configure NXAPI/Openflow in TLS mode according to user Requirements. Using this tool Cisco Nexus Data Broker will be configured with the required certificates and it should be started in the secure mode. When Cisco Nexus Data Broker is started in TLS mode, all devices will be connected in secure mode.

## Slide 5: TLS Script - Prerequisites
Ensure that OpenSSL is installed on the Linux host
Python
Pip
pexpect
yaml
requests
Paramiko
Telnet
Java 8

## Slide 6: TLS NXAPI Script usage
Clone the code from the below link.
git clone https://github.com/datacenter/nexus9000.git
Navigate to following path:
cd nexus9000/
cd nexusdatabroker/
cd TLSNXAPITool1.0/
The script can run in 2 ways.
1) After running python script using following command :
python TlsNxapiTool.py
Logs will be shown in console as well as in log file
2) After running python script using following command :
python TlsNxapiTool.py --quiet
Logs will be shown only in log file.

## Slide 7: TLS NXAPI Script Input and Logs
The input file is present in corresponding path –
TLSNXAPITool1.0/Utilities/Input/inputfile.yaml
IP:
IP1:
port: 443 # can be any port number
address: 10.16.206.127
username: admin
password: cisco123
ServerIP:
ServerIP1: # Can give any number of servers
ip: 10.16.206.179
user: root
password: cisco123
path_ndb_build: /root/Ndb3.2-Releasebuild/xnc/configuration # NDB build path to be given till xnc folder

## Slide 8: TLS NXAPI Script Input and Logs
The key value should be mentioned as following :Certificates will be generated using provided key value
Key_Password: 'cisco123‘
NDB Login credentials
xnc_password: 'admin'
xnc_username: 'admin'
In order to change values provide corresponding information for following fields.
If info not provided for following fields by default certificates will be generated using following values.
commonName_default = www.cisco.com
0.organizationName_default = Cisco
localityName_default = San Jose
stateOrProvinceName_default = CA
countryName_default = US
emailAddress_default = webmaster@cisco.com
organizationalUnitName_default = NDB
By default Input file consists 2 servers and 2 devices info
If tool is using for following combination and 2nd server and 2nd device details should be commented out.

## Slide 9: NXAPI TLS Script Logs
The logs can be seen in 2 ways.
1) After running python script using following command :
python TlsNxapiTool.py
Logs will be shown in console as well as in log file
2) After running python script using following command :
python TlsNxapiTool.py --quiet
Logs will be shown only in log file.

## Slide 10: Openflow TLS script usage
Clone the code from the below link.
git clone https://github.com/datacenter/nexus9000.git
Navigate to following path:
cd nexus9000/
cd nexusdatabroker/
cd TLSOPENFLOWTool1.0/
The script can run in 2 ways.
1) After running python script using following command :
python TLSScriptOF.py
Logs will be shown in console as well as in log file
2) After running python script using following command :
python TLSScriptOF.py --quiet
Logs will be shown only in log file.

## Slide 11: Openflow TLS script Input and Logs
The input file is present in corresponding path –
TLSOPENFLOWTool1.0 /Utilities/Input/inputfile.yaml ( This can be changed according to server/switch used same as NXAPI)
IP:
IP1: # Can give any number of devices
address: 10.16.206.116
username: admin
password: cisco123
ServerIP:
ServerIP1: # Can give any number of servers
ip: 10.16.206.160
user: root
password: cisco123
path_ndb_build: /root/Ndb3.3-Releasebuild/xnc # NDB build path to be given till xnc folder

## Slide 12: TLS Openflow script Input and Logs
Log file generated - TLSOPENFLOWTool1.0 /Utilities/Log/Logfile.log
Once python runs successfully add openflow controller to NDB .If NDB is running in HA(Cluster) mode add all openflow controllers to NDB .
Steps -
FOR NXOS below I5 version
switch(config)# openflow
switch(config-ofa)# switch 1
switch(config-ofa)# tls trust-point local myCA remote myCA
switch(config-ofa-switch)# pipeline{201/203}
switch(config-ofa-switch)#controller ipv4 {A.B.C.D} port 6653 vrf management security tls
FOR NXOS above I5 version
switch(config)# openflow
switch(config-ofa)# switch 1 pipeline 201
switch(config-ofa)# tls trust-point local myCA remote myCA
switch(config-ofa-switch)#controller ipv4 {A.B.C.D} port 6653 vrf management security tls

## Slide 13: TLS Openflow script Input and Logs
The key value should be mentioned as following :Certificates will be generated using provided key value
Key_Password: 'cisco123‘
NDB Login credentials
xnc_password: 'admin'
xnc_username: 'admin'
In order to change values provide corresponding information for following fields.
If info not provided for following fields by default certificates will be generated using following values.
commonName_default = www.cisco.com
0.organizationName_default = Cisco
localityName_default = San Jose
stateOrProvinceName_default = CA
countryName_default = US
emailAddress_default = webmaster@cisco.com
organizationalUnitName_default = NDB

## Slide 14: Limitations
Only self signed TLS certificate is supported.
Script is tested on Ubuntu server currently.
Known caveats
CSCvf07022 | Created certificates and files are still present Once script terminates in middle of execution

## Slide 15: FAQ’s
If user hits this case - Device 10.16.206.116 Failed to authenticate trustpoint myCA while accepting certificate Device and server timings not matching
The server and device time should match .So user has to set server time as a device time.
In Centos script execution server-
After Installing Java 8 ,The path should not be set in file (Permanently ). If java path sets permanently the server will get hang and no commands will work
The User has to export everytime -
Steps-
export JAVA_HOME=/opt/jdk1.8.0_141
export JRE_HOME=/opt/jdk1.8.0_141/jre
export PATH=$PATH:/opt/jdk1.8.0_141/bin:/opt/jdk1.8.0_141/jre/bin
If user hit any proxy issue while adding device user has to unset proxy which is configured .Steps-
[root@ucp-ctrl-3 TLSNXAPITool1.0]# unset http_proxy
[root@ucp-ctrl-3 TLSNXAPITool1.0]# unset https_proxy